## Slide 1: Predictive maintenance using ML for printheads
Presented by: Anthony Atallah
Supervisor: M.Wolf Beat
Company representative: M.Fernando Rodriguez Llorente

## Slide 2: Agenda
Context & problematic
Data + physics
Pipeline (ML)
Results + discussion

## Slide 3: Context
Working with iPrint, leading research institute in 2D/3D printing technologies.

## Slide 4: Printhead
Component in a printer that holds and transfer the ink to the printing medium
1280 nozzles separated into 4 electrical banks: A, B, C & D

## Slide 5: Problematic
Nozzle failures = print defects = cost/downtime
Current maintenance is reactive and depends on visual inspection or periodic cleaning.
Leverage signals for a proactive approach to maintenance.

## Slide 6: What we measure
Self-sensing waveform → nozzle dynamics
Nozzle-check image → label per nozzle

## Slide 7: Self-sensing waveform
The same piezo element that actuates also senses ring-down via the direct piezoelectric effect.

## Slide 8: How labels are produced
Proprietary algorithm that segments and labels printed patterns
4 possible labels :
Jetting
Non-jetting
Intermittent
Deviated

## Slide 9: Project scope
1. Relate signals to defect mechanisms
Explore link between applied pressure and acoustic signature.
2. Dynamic prediction of defects
Predict jetting status.
3. Proof-of-concept demonstrator
Input: acoustic data → Output: jetting status / early warnings.

## Slide 10: Key contributions
Built preprocessing + parametric fitting pipeline
Trained/evaluated models across multiple test regimes
Identified defect dynamics + limitations

## Slide 11: Controlled pressure sweeps to induce defects
Lowering sweep: −50 → −87.6 mbar (95 steps)
Increasing sweep: −50 → −46 mbar (11 steps)
Pressure = meniscus pressure (ink system vs atmosphere)
2 replicates per sweep: rep1 & rep2

## Slide 12: Dataset: lowering replicate 1
1280 nozzles × 95 pressure levels = 121,600 labeled waveform instances for the main sweep

## Slide 13: We keep the informative part only
First 35-time sample discarded:
Correspond to the saturated state after the actuation

## Slide 14: Compact, interpretable features
6 fitted parameters:

## Slide 15: Robust fitting in 3 steps
Initial parameters estimates
Windowed least-square error fitting + overlap-add
Weighted average parameters

## Slide 16: Fitting results

## Slide 17: Parameters overview
and fluctuates the most at extremities.

## Slide 18: Defects concentrate at extremities
Dataset | Jetting | Non-jetting | Intermittent | Deviated
Lowering rep. 1 | 117,375 | 2,938 | 507 | 777
Increasing rep. 1 | 12,506 | 1,173 | 13 | 353

## Slide 19: Parameters in function of labels
Boxplot midline represents the median.
Large difference between “Jetting” and “Non-jetting”

## Slide 20: Binary labels for learning
Intermittent/deviated are unstable across steps.
We focus on the most reliable target: Jetting vs Non-jetting.

## Slide 21: Experiments & results
3 tasks:
Classification: jetting vs non-jetting per (nozzle, pressure)
Pressure regression: predict pressure with parameters.
Predictive maintenance: “will this nozzle flip to non-jetting later?” lead time K

## Slide 22: Classification model
Input: fitted ring-down parameters
Model used: Histogram-based Gradient Boosting (HGB)
chosen for non-linear interactions + robustness on tabular features
Splitting rule: balanced set, group split by nozzle ID a nozzle never appears in both train and test (prevents leakage across pressures)
4 evaluation settings (classification):
  Held-out balanced test: equal Jetting/Non-jetting in test
  Full test excl. train: evaluate on the full remaining distribution (imbalanced)
  Cross-replicate transfer: test on Lowering rep2
  Cross-sequence transfer: test on Increasing rep1
Dataset | Jetting | Non-jetting
Lowering rep. 1 | 117,375 | 2,938

## Slide 23: Metrics
Accuracy: the proportion of correctly classified instances.
Precision: the fraction of predicted positives that are correct.
Recall: the fraction of actual positives that are detected.
score: the harmonic mean of precision and recall.

## Slide 24: Classification: results
Evaluation set | #Jetting | #Non-jetting | Accuracy | Precision | Recall | F1
Lowering rep. 1 (balanced test) | 501 | 501 | 0.99 | 1.0 | 0.99 | 0.99
Lowering rep. 1 (full excl. train) | 114,938 | 501 | 0.99 | 1.0 | 0.99 | 0.99
Lowering rep. 2 (full) | 116,837 | 3,139 | 0.99 | 1.0 | 0.99 | 0.99
Increasing rep. 1 (full) | 12,506 | 1,173 | 0.95 | 1.0 | 0.95 | 0.97
Detection is near-perfect on lowering sweeps and remains strong when changing replicate and trajectory.

## Slide 25: Classification: discussion
Variable | Distance correlation with label
Frequency f | 0.86
Phase ϕ | 0.60
Meniscus pressure | 0.22
Label correlates strongly with oscillation parameters (f, φ).
Defects are concentrated in the low-pressure tail → confounding risk → motivates pressure-matched evaluation.

## Slide 26: Pressure regression
Metric | Value
R² | 0.51
MAE | 6 mbar
RMSE | 7.7 mbar
Pressure can be predicted from the fitted parameters.

## Slide 27: Predictive maintenance: model
Model used: Histogram-based Gradient Boosting (HGB)
Splitting rule: balanced set, split by nozzle ID
4 evaluation settings (classification)
Jetting=829 | Non-Jetting=433

## Slide 28: Predictive maintenance: results

## Slide 29: Predictive maintenance: results
K | Dataset | #Won’t flip (0) | #Will flip (1) | Accuracy | Precision | Recall | F1
1 | Lowering rep. 1 (balanced) | 85 | 85 | 0.88 | 0.93 | 0.81 | 0.87
 | Lowering rep. 1 (full) | 170 | 85 | 0.86 | 0.78 | 0.81 | 0.79
 | Lowering rep. 2 (full) | 832 | 441 | 0.87 | 0.79 | 0.86 | 0.82
 | Increasing rep. 1 (full) | 538 | 713 | 0.76 | 0.75 | 0.88 | 0.81
2 | Lowering rep. 1 (balanced) | 85 | 85 | 0.67 | 0.81 | 0.45 | 0.58
 | Lowering rep. 1 (full ) | 170 | 85 | 0.75 | 0.68 | 0.45 | 0.54
 | Lowering rep. 2 (full) | 832 | 441 | 0.74 | 0.68 | 0.47 | 0.55
 | Increasing rep. 1 (full) | 538 | 713 | 0.52 | 0.69 | 0.29 | 0.40

## Slide 30: Use-case
Input: self-sensing waveform (per nozzle)
Pre-process + fit parametric model
TRAIN MODEL WITH FITTED PARAMETERS
Output: K = 1 prediction

## Slide 31: Limitations + next steps
Limitations:
Defects induced by pressure, not long-term wear
Binary labels only; intermittent/deviated excluded
Generalization to other printheads still to validate
Fitting doesn’t account for local variations
Next steps:
Collect stable-operation datasets (natural clogging/wear)
Richer representations e.g. spectrograms or neural embeddings
Add spatial context (column-aware models)

## Slide 32: Conclusion
What was built: end-to-end pipeline from ring-down → features → models
What was achieved: strong defect detection + early-warning performance ()
What remains: test our models/observations on wear and tear induced datasets

## Slide 33: Thank you for listening!

## Slide 34: Annex: Parameter initialization
: estimate from the peak of the tapered FFT magnitude, refined by parabolic interpolation.
: obtain from the peak-to-peak range of the detrended signal.
detect peaks in the absolute detrended signal and fit a line to the logarithm of peak magnitudes versus time; the slope yields an estimate of the decay rate.
: estimate from the signal value and its initial slope.
, : least squares fit.

## Slide 35: Annex: Bank phase correction

## Slide 36: Annex: parameters

## Slide 37: Annex: parameters

## Slide 38: Annex: Distance correlation
A non-parametric measure of dependence that captures non-linear relationships between variables and is not sensitive to the scale of data.

## Slide 39: Annex :Predictive maintenance

## Slide 40: Annex : Gantt Chart